## Slide 1: Lenet Accelerator Final Presentation
第七組
翁啟文、賴柏光、羅允辰

## Slide 2: Outline
Recap
P&R result
Post-layout simulation

## Slide 3: Recap

## Slide 4: Basic Workflow(HW5)
CONV1
SRAM A0-A8
SRAM B0-B8
SRAM_CONV
CONV2
FC1
SRAM E
SRAM F
SRAM_FC
FC2
Optimization:
Reduce area (CONV1+CONV2 & FC1+FC2)
Split pipeline (CONV & FC)
Pre-sim & gate-level sim result:
  cycle count: 20770
  cycle period: 4 ns
  area: 77292.340211 um2
Origin
Overlap

## Slide 5: P&R result

## Slide 6: P&R Layout
Core area:
397.393 * 396.200 = 157447.1066 um2
Core area: 88755.872684 um2
Utility: 56.37%
CONV_control
CONV_datareg
CONV_multiple_compare
FC_control
FC_multiple_accumlator
Quantize
CONV + FC

## Slide 7: P&R timing and power
Timing:
  P&R clock period: 4.2ns (less than 1.1* Synthesis clock period = 4.4ns)
Power consumption (from ICC analysis):
  1st : combinational logic circuit: 46%
  2nd: register: 42%
  3rd: clock: 12%
 |  | ICC analysis | Prime Time analysis
Dynamic Power | Internal | 3.4918 mW (54.45%) | 2.634 mW (47.13%)
 | Switching | 1.5274 mW (23.82%) | 1.548 mW (27.70%)
Leakage Power |  | 1.3933 mW (21.73%) | 1.406 mW (25.17%)
Total Power |  | 6.4125 mW | 5.589 mW

## Slide 8: DRC and LVS verification
Pass DRC verification
There are 2 errors in LVS verification
  Two short nets are detected.
However, our post layout simulation
have passed (strange…).

## Slide 9: Post-layout simulation

## Slide 10: Result
cycle period in testbench: 10ns
SRAM read data delay: 0.3*cycle period
I/O external delay: 2ns (half of synthesis clock period)
Total cycle counts:
  CONV+FC: 19736 + 20770 = 40506
  In reality, only 20770 cycles required due to our pipeline design

## Slide 11: Snapshots